## Slide 1
Arduino Leonardo, Micro or ProMicro
MCP4725
external i2C 12bit DAC
Wiring diagram for external DAC’s (only valid for firmware with option “g”, in DAC± mode)
Arduino MCP4725
5V VDD
GND GND
2 SDA (i2C data)
3 CLK (i2C clock)
DAC0 - ADDR pin to GND
i2C address 0x60 is for left force
DAC1 - ADDR pin to VCC
i2C address 0x61 is for right force
DAC0
0x60
left
DAC1
0x61
right
+
-
+Vcc
-Vcc
output ±10V
Vcc can be provided by
regulated bipolar power supply
use LM7812, LM7912 for ±12V
or LM7815, LM7915 for ±15V
IC1
IC1 - can be any audio grade
operational amplifire like
TL072, NE5532 or equivalent
10k
10k
20k
20k
shielded audio grade cable
goes to AASD analog input
use of analog optocoupler
is desired but not required