## Slide 1
Arduino Leonardo, Micro or ProMicro
Wiring diagram for HX711 chip and load cell (only valid for firmware with option “l”)
LC HX711 Arduino
VCC 5V
GND GND
DT 4
SCK 5
red E+
black E-
white A+
green A-
E+
E-
A+
A-
LC - 4 wire load cell (full bridge)
if nothing is happening with the brake
pedal, you may try to swap A- and A+
wires on the load cell, because your
load cell may output a reversed voltage
it is recommended to use a shielded cable
between HX711 and a load cell in order to
reduce signal noise as much as possible
you can set HX711 in 80Hz
mode by manually soldering
pin 15 to VCC, some traces
may need cutting to avoid
shorting, so please be careful
red
black
white
green