## Slide 1
Arduino Leonardo, Micro or ProMicro
MCP4725
external i2C 12bit DAC
Wiring diagram for external DAC’s (only valid for firmware with option “g”, in 2CH DAC0-50-100 mode)
Arduino MCP4725
5V VDD
GND GND
2 SDA (i2C data)
3 CLK (i2C clock)
DAC0 - ADDR pin to GND
i2C address 0x60 is for x-force
DAC1 - ADDR pin to VCC
i2C address 0x61 is for y-force
Analog output direction:
0V - negative force
2.5V - zero force
5V - positive force
DAC0
0x60
xFFB
DAC1
0x61
yFFB
output (0-5)V for y-axis FFB
output (0-5)V for x-axis FFB
2x twisted pair
or shielded cables