## Slide 1
Arduino Leonardo, Micro or ProMicro
Wiring diagram for double AS5600 magnetic encoder (only valid for firmware v250 and later with options “b” + “w” + “u”)
AS5600x
Arduino TCA9548A AS5600x AS5600y
5V VCC VCC VCC
GND GND GND, DIR GND, DIR
SDA
CLK
    SD0 SDA
    SC0 SCL
    SD1 SDA
    SC1 SCL
AS5600y
i2C multiplexer
TCA9548A
An i2C multiplexer chip like TCA9548A gives us a possibility to connect eight i2C devices with the same address to a single host bus. Two output i2C bus channels (0 and 1) are used to connect two AS5600 magnetic encoders with the same address (0x36). Firmware takes care of channel switching and reading of an individual angle values, which are then processed with multiturn feature and used as 2-axis input (X and Y).